## Slide 1: P&T challenges during deinventory of legacy facilities
drhgfdjhngngfmhgmghmghjmghfmf
Dan Pancake
Project Manager
Nuclear Facilities Deactivation
dpancake@anl.gov
Jeff McGhee
Transportation Nuclear Facility Manager
ESH and P&T Lead for Deinventory
jmcghee@anl.gov
Contractor’s Transportation Management Association Meeting
May 2017, Point Clear, AL
CTMA 2017

## Slide 2: DEACTIVATION AND DEINVENTORY
Alpha Gamma Hot Cell Facility
  ~66X HC2 SOF
  Irradiated Fuel Samples and Test Specimens (Fuel Examination Waste)
  Sodium Bonded Fuel Debris & Pin Fragments
Building 205 K-Wing Hot Cell Complex
  Separations Science Byproducts
  ATM Standards (Additional FEW)
Building 200 MA Wing Hot Cell Complex
  Irradiated Neutron Sources
  Higher Energy Gamma Source Materials
  “XYZ” Box and Other “Home Made” Source Materials
Legacy Materials in the Waste Management Facilities
  CP5 Shield Plug Assemblies
Building 350 (Formerly New Brunswick Laboratory)
  Transuranic Metals and Oxides in type B Quantities / Unique Containment
National TRU Program Support for RH TRU Disposition
  Shielded Container Assemblies
Facilities Deactivation Activities That Generated Packaging and Transportation Challenges

## Slide 3: DEACTIVATION AND DEINVENTORY
Work with National TRU Program on Pilot Project
Shielded Container Assembly (SCA-1)
  Used as an approved overpack for disposition of certain RH TRU debris containers as CH TRU Packages at WIPP
  Provides shielding via one-inch lead layer between the containment surfaces.
  Shipped in the HALF-PACT to WIPP
  Disposed above grade, as other CH TRU Packages
  Licensed content in the TRUPACTs
  ANL partnered with NWP to execute the pilot program for loading and shipping in 2013 (9 SCA-1s)

## Slide 4: Challenge 1
“Cheap to Keep” facilities don’t often function as designed
  Doors don’t open
  Lights don’t turn on
  Hoists don’t work or have not been serviced
  Floor storage corroded or has water seepage
  Packaging used is *vintage* now, and likely not compliant
    6M’s
    Gaskets that dry rot
Can you get to the material?

## Slide 5: Challenge 2
Understanding what you really have
Often requires extensive NDA/NDE and legacy data gathering, where data are available at all
Legacy facilities sometimes have no living souls left to consult with
Handwritten notebooks…well
  If you can read them
  Stylistic differences in data recording methodology can be a challenge
  Incomplete information (think batch division and consumed)
SURPRISE!
  Is that what we think it is?
  Does someone really want that?
What is that?

## Slide 6: Challenge 3
No authorized packaging for that material/activity
Creativity in description to better match material
  Mixed fission products
  Fuel Examination Waste
Regulatory approval process for content modification is
  Costly
  Lengthy
  Requires good coordination
  PCP assistance is ESSENTIAL for success
We used to ship that in a 6M all the time…

## Slide 7: Challenge 4
What requirements apply to your “stuff”?
  Who needs to be involved, and when, will certainly vary with material
  What was done in 1992 is NOT the same as today
  Coordination with package owner essential, as resources and expectations may be different when working with DOE versus NRC
  Have “road ready” packages to take advantage of available Bandwith
Coordination with EM, NNSA, Security, States, Disposition Sites

## Slide 8: Challenge 5
Older, unique or high activity materials that have source capability may be OSRP candidates
Coordination with OSRP for contents authorization for special form capsules important
QA procedures for “filling and fabrication” of OSRP capsules can be coordinated
  Additional time needed
  Dedicate a staffer or two to be trained to allow continued operation
Intermediate storage and ultimate shipping difficult for Type A, high dose neutron sources
  RaBe, AmBe, PuBe and Cf need S100 packaging, or custom fabricated and tested
Source Materials Are Unique, OSRP CAN Help!

## Slide 9: Challenge 6
Don’t shy away from engineering evaluation and solutions. Packages can be fabricated for a given package to deal with high dose issues
  RaBe and Co content needed special inner container for dose
Design your own solutions for use with packages
  Partner with manufacturers/fabricators
  Use COTS and retest for Type A, then split your stuff to “fit”
Wow, that is a LOT, or not something we see…we don’t have anything for that

## Slide 10: Challenge 7
Most legacy facilities have limited operations that are authorized.
If the target material(s) is/are not in exactly the configuration for authorized content…
  Content modification may be needed
  Engineered solution may be needed
  Get PCP and package owner involved EARLY
  DOE/NNSA “ownership” coordination needs to happen at your site office/program office level
Yep that material is authorized, but the primary containment, like glass bottles, is not…

## Slide 11: Challenge 8
If there is a concept or idea that may be of benefit to others with similar materials or issues in the DOE Complex, push forward…
  Resistance to change can be hard
  Intellectual property and process can be a challenge and take up time
  Costs initially…vary a great deal, long term savings must be balance funding, safety, and return on investment
Convincing your DOE partners and your management to let you be a pioneer of new processes/ideas

## Slide 12: Challenge 9
Know your design solutions
  Sodium bonded fuel needed special solutions for FEW into tubes, into racks that will fit with transport cask chosen
  Be sure you have a listing of Q and non-Q parts and features PRIOR to acceptance, even if contracting others to do the work
  When problems arise PCP is your pathway to solutions!
There will be an issue…be ready…stay calm…

## Slide 13: Challenge 10
Work with a vendor and/or other DOE sites to find a solution
Deal with the off-spec and “no reuse path” materials as waste
Work with your MC&A Team, as well as DOE Site Office, to ensure material can be wasted
Develop new and novel methods to handle unusual materials
There is no packaging solution. We don’t know what it is. Now what?

## Slide 14
Questions?